## Slide 1
Cloud-Native
Broadband Edge
Deploying a High-Performance vBNG on Kubernetes
A 10-minute overview of architecture, packet I/O, routing integration, and operational design.
KUBERNETES
DPDK / VPP
HELM
Presented by Christopher Adigun • October 2026
01
Notes: Open with the central question: can Kubernetes host a broadband edge function while preserving predictable packet I/O and familiar routing behavior? This presentation covers the BNG role, the Kubernetes architecture, the packet path, NIC acceleration, and a practical production blueprint. High availability is included as a simple design consideration rather than the main topic.

## Slide 2
SPEAKER INTRODUCTION
Christopher Adigun
Cloud-Native AI & Telecom Architect
Areas of focus
Cloud-native telecom platforms
AI-assisted network operations
Kubernetes data-plane design
Perspective
Connecting telecom packet processing with cloud-native lifecycle management and practical automation.
Disclaimer
The views expressed in this presentation are my own and do not represent those of my employer.
02
Notes: Briefly introduce yourself as Christopher Adigun, a Cloud-Native AI and Telecom Architect. Mention your focus on telecom platforms, network automation, and Kubernetes data planes. State the disclaimer clearly: the views in this presentation are personal and do not represent those of your employer. Keep this introduction to about 40 seconds.

## Slide 3
PROJECT USED
OSVBNG: an open-source virtual BNG
The project combines a Go control plane with VPP, FRR, and DPDK.
Why OSVBNG
Open-source BNG for standard x86 servers
IPoE and PPPoE subscriber access
CGNAT, routing, AAA, QoS, and monitoring
Container image and declarative configuration
Runtime stack
OSVBNG control plane
Subscriber lifecycle
configuration and APIs
VPP + DPDK
Fast packet processing
and NIC access
FRR routing
Prometheus metrics
Project: github.com/veesix-networks/osvbng
03
Notes: Introduce the specific project used in the deployment: OSVBNG from veesix-networks. The project provides an open-source BNG control plane and integrates VPP, FRR, and DPDK. It supports IPoE and PPPoE access, CGNAT, routing, AAA, QoS, and monitoring. The Kubernetes work packages this software as a StatefulSet and supplies deterministic interfaces, configuration, and lifecycle management. Source: https://github.com/veesix-networks/osvbng

## Slide 4
1 • THE ROLE
The BNG is the subscriber edge control point
It joins subscriber access, policy, addressing, routing, and internet reachability.
1
Session control
IPoE / DHCP sessions
subscriber lifecycle
2
Policy + AAA
RADIUS-backed identity
and service policy
3
Traffic services
CGNAT, QoS, counters
and forwarding
4
Core routing
BGP reachability
toward the ISP edge
Key design question
Can these functions become schedulable, observable workloads without losing deterministic packet I/O?
Source: veesix-networks/osvbng project overview and feature list.
04
Notes: Explain the BNG in operator language. It terminates subscriber sessions, applies identity and policy, assigns addresses, provides services such as CGNAT, and exchanges routes with the provider core. Kubernetes does not remove those responsibilities. It changes how the function is packaged, placed, upgraded, and observed. Source: https://github.com/veesix-networks/osvbng

## Slide 5
2 • THE DESIGN
One cluster, explicit data-plane interfaces
Management stays Kubernetes-native. Subscriber and core traffic use Multus plus VFIO-bound virtio NICs.
UE generator
BNG Blaster
VLAN sessions and tests
OSVBNG StatefulSet
VPP + DPDK
subscriber forwarding
FRR edge routers
BGP toward the BNG
and MikroTik
MikroTik / Internet
Default route
and return path
Subscriber access
VLANs 100–119
BNG–FRR transit
172.31.255.0/29
FRR–MikroTik uplink
192.168.88.12 / .13
Upstream LAN
192.168.88.0/24
Kubernetes manages placement, restart, configuration, secrets, and observability.
Example addresses: FRR-A 192.168.88.12/24 and FRR-B 192.168.88.13/24.
05
Notes: Walk left to right. UE test workloads generate VLAN-tagged subscribers. The BNG StatefulSet owns dedicated VFIO devices and runs VPP with DPDK. FRR pods use Multus macvlan interfaces and exchange BGP with both BNG members. The upstream side uses 192.168.88.12 and .13, avoiding the previously assigned .250 and .251 addresses. Kubernetes handles lifecycle and management traffic; the forwarding path remains explicit.

## Slide 6
KUBERNETES INTEGRATION
Plugins and live workload state
Secondary networks and device allocation remain explicit.
Networking and device plugins
Multus CNI
Attaches access, core, and uplink networks
SR-IOV Device Plugin
Advertises two VFIO virtio NICs per BNG pod
host-device CNI
Moves assigned interfaces into the BNG pod
macvlan CNI
Connects FRR core and upstream interfaces
LIVE CLUSTER SNAPSHOT • kubectl get pods -n osvbng-ha
NAME READY STATUS NODE
osvbng-0 1/1 Running node-01
osvbng-1 1/1 Running node-02
osvbng-frr-isp-a 1/1 Running node-02
osvbng-frr-isp-b 1/1 Running node-01
osvbng-freeradius 1/1 Running node-03
osvbng-radius-postgresql-0 1/1 Running node-03
FRR-A BGP snapshot
BNG-A: Established, 1 prefix BNG-B: Established
MikroTik: pending peer update
Observed from the running cluster on 10 October 2026.
06
Notes: List the Kubernetes integrations actually used. Multus attaches multiple networks. The SR-IOV Device Plugin advertises the VFIO-bound virtio devices as Kubernetes resources. The host-device CNI moves the assigned access and core devices into the BNG pod. Macvlan provides FRR core and upstream interfaces. The snapshot on the right comes from the running osvbng-ha namespace and shows both BNG pods, both FRR pods, FreeRADIUS, and PostgreSQL. FRR-A had established BGP sessions with both BNG members when observed.

## Slide 7
3 • THE PACKET WALK
From a subscriber packet to the internet and back
The route exchange is as important as the fast path.
1
Attach
DHCP / IPoE
creates a UE session
2
Classify
VLAN and policy
select service
3
Translate
CGNAT maps UE
to public pool
4
Route
BGP selects an
FRR next hop
5
Return
MikroTik learns
the CGNAT prefix
Proof point
A successful ping validates session state, CGNAT, BGP, the upstream default, and the return route.
Operational checks use BGP summaries, routes, pod interfaces, and subscriber traffic.
07
Notes: Use this as the demo setup. A subscriber first gets a session and address. The BNG classifies the VLAN and service, performs CGNAT, and forwards toward an FRR next hop. FRR receives subscriber and CGNAT reachability from the BNG and the default route from the upstream router. Return traffic only works when the upstream learns the translated prefix. This is why a ping is an end-to-end proof, not just an ICMP check.

## Slide 8
4 • WHY THIS IS PRACTICAL NOW
The NIC is becoming part of the edge compute platform
DPDK, SR-IOV, SmartNICs, and DPUs shift packet work away from general-purpose CPU cores.
Traditional edge
BNG appliance
Router appliance
Security appliance
Consolidated Kubernetes edge
vBNG
DPDK / VPP
FRR
BGP routing
Services
AAA / observability
Shared lifecycle • explicit resource isolation • fewer edge boxes
NIC OFFLOAD
Design caveat: consolidation reduces boxes, not failure domains. Keep resource isolation and simple HA where service continuity matters.
Sources: NVIDIA BlueField/DOCA documentation; Intel Network Builders cloud-native BNG white paper.
08
Notes: This is the strategic point. High-speed NICs, SR-IOV, DPDK, SmartNICs, and DPUs increasingly provide acceleration and isolation. At smaller edge sites, that can make separate hardware for each network function unnecessary. A shared Kubernetes cluster may host the vBNG, software routers, AAA, and observability. Be careful with the claim: consolidation is an option, not a universal prescription. Capacity, blast radius, and operational policy still decide the production design. Sources: https://networking-docs.nvidia.com/bf3dpu/introduction and https://networkbuilders.intel.com/docs/networkbuilders/re-architecting-the-broadband-network-gateway-bng-in-a-network-functions-virtualization-nfv-and-cloud-native-world-1633374232.pdf

## Slide 9
5 • PRODUCTION BLUEPRINT
A repeatable broadband edge, delivered as Helm charts
Start with explicit resource boundaries and a testable failure model.
1
Capacity profile
Subscriber target, CPU, hugepages, and NIC queues
2
Data-plane placement
Dedicated VFIO resources and topology-aware affinity
3
Routing integration
BGP to redundant FRR instances and upstream return routes
4
Operations
Versioned Helm releases, metrics, logs, and rollback
5
Availability
Two placements, anti-affinity, and recovery testing
Takeaway
Kubernetes can host the broadband edge when packet I/O remains explicit.
Package the function.
Reserve the resources.
Test the complete path.
Reference implementation: github.com/infinitydon/cloud-native-vbng-edge-lab
09
Notes: Close with a production sequence. Define the subscriber scale and hardware profile first. Reserve the data-plane resources and place workloads according to topology. Integrate routing so both the default route and return prefixes are correct. Operate the solution through versioned Helm releases and observable health checks. For availability, keep the baseline simple: two placements, anti-affinity, and tested recovery behavior. The main takeaway is that Kubernetes can host the broadband edge when packet I/O remains explicit.

## Slide 10
CLOSEOUT
Optional MCP and AI operations layer
Keep the automation layer separate from the network-function Helm charts.
Operations UI
Natural-language queries
and formatted responses
AgentGateway
Authentication
and tool authorization
ToolHive + MCP
Managed MCP servers
and tool discovery
BNG + Kubernetes
Health, sessions, BGP,
routes, and diagnostics
Practical next step
Start with read-only diagnostics, role-based tools, evidence in every response, and approval before changes.
OPTIONAL
This MCP and AI layer is a separate deployment and is not included in the vBNG Helm chart.
Demonstrated separately with AgentGateway, ToolHive, Open WebUI, and OSVBNG MCP tools.
10
Notes: Close with the path beyond the deployment itself. A separate operations layer can expose read-only BNG and Kubernetes diagnostics through MCP tools. AgentGateway provides the security boundary, ToolHive manages MCP servers, and an operations UI presents well-formatted answers. Start with health, BGP, routing, and subscriber visibility. Require authorization and approval before any change. Emphasize that this layer remains a separate deployment and does not belong inside the vBNG Helm chart.